## Slide 1: Ad-Hoc WiFi Collision Avoidance Problem

## Slide 2: Scenario settings
Transmission Power: 100mW,12Mbps
Noise: -100dBm
Receive power sensitivity: -105dBm
below this threshold a signal is considered as
noise instead of a packet for collision avoidance
R1
S1
R2
S2
185m
185m

## Slide 3: Scenario settings
Transmission Power: 100mW,12Mbps
Noise: -100dBm
Receive power sensitivity: -105dBm
Node S1 sends RTS (for R1)
  Received by R1 , SNR ~1.3dB
  Ignored by S2,R2 (low receive power)
R1
S1
R2
S2
185m
570m
-99dBm
-116dBm
-119dBm
475m
RTS

## Slide 4: Scenario settings
Transmission Power: 100mW,12Mbps
Noise: -100dBm
Receive power sensitivity: -105dBm
Node R1 sends CTS (for S1)
  Received by S1 , SNR ~1.3dB
  Ignored by S2,R2 (very low receive power)
R1
S1
R2
S2
185m
390m
-99dBm
-109dBm
-115dBm
235m
CTS

## Slide 5: Scenario settings
Transmission Power: 100mW,12Mbps
Noise: -100dBm
Receive power sensitivity: -105dBm
Node S2 sends RTS (for R2)
  Received by R2 , SNR ~1.3dB
  Ignored by S1,R1 (very low receive power)
R1
S1
R2
S2
185m
570m
-99dBm
-116dBm
-119dBm
475m
RTS

## Slide 6: Scenario settings
Transmission Power: 100mW,12Mbps
Noise: -100dBm
Receive power sensitivity: -105dBm
Node R2 sends CTS (for S2)
  Received by S2 , SNR ~1.3dB
  Ignored by S1,R1 (very low receive power)
R1
S1
R2
S2
185m
390m
-99dBm
-109dBm
-115dBm
235m
CTS

## Slide 7: Scenario settings
Transmission Power: 100mW,12Mbps
Noise: -100dBm
Receive power sensitivity: -105dBm
S1 and S2 transmit long data
packets in parallel!
Interfere with each other
Causing high PER (~60%)
R1
S1
R2
S2
DATA
DATA

## Slide 8: Proposed solution
Detect RTS packet in longer range
Transmit 3 times short RTS packet
  Receivers senses 3 short close “noises” -> “RTS”
  Receivers stay quiet throughout packet duration
Can use other means for RTS:
different signal form
higher power or etc.
R1
S1
R2
S2
RTS
RTS
RTS