## Slide 1: Real Time Video Streaming in Multi hop Ad-Hoc Wireless networks
Yaniv Fais
Under supervision of Prof. Guy Even
Joint work with Prof. Guy Even, Moti Medina,
Moni Shahar and Alexander Zadorojniy

## Slide 2: Background
Research part of consortium dedicated to communication for rescue teams
  Quick deployment (no backbone)
  Common technology (WiFi)
  Dedicated system
Focused on video data
Practical solution
2

## Slide 3: Agenda
Problem Definition
  Real-Time Video
  WiFi introduction
Routing & Scheduling
  Interference models
Simulator
  Flow Control
Experimental results
  Video transmission
3

## Slide 4: Problem Definition
Ad-Hoc Wireless Network model
  Nodes in the plane , know location and time (using GPS)
  Nodes with single radio
  Multiple radio channels
4

## Slide 5: Problem Definition II
Input:
  Nodes / locations / transmission power
  real-time video transmission requests:
  Source , Destination , Bandwidth
  (Source and destinations may not be neighbors)
Goal: serve requests fairly (maximize min-throughput)
5

## Slide 6: Real-Time Video characteristics
High-bandwidth
  ~1Mbps after encoding
Require: low end-to-end delay
  Few seconds at most
Require: small packet-loss
  < 5%
Adjustable bit rate because encoder can be controlled (variable quality and compression ratio)
6

## Slide 7: IEEE 802.11g (WiFi)
Carrier sense multiple access with collision detection (CSMA/CD)
Transmitter sends Request To Send (RTS)
7

## Slide 8: IEEE 802.11g (WiFi)
Receiver sends “Clear To Send” (CTS)
All other nodes remain “quiet” throughout packet transmission
8

## Slide 9: IEEE 802.11g (WiFi)
Transmitter sends frame with payload data (large frame – several KB)
9

## Slide 10: IEEE 802.11g (WiFi)
Receiver sends “Acknowledge” (ACK) packet once completed
10

## Slide 11: IEEE 802.11g (WiFi)
Distributed protocol that avoids collisions
But: (In multi-hop setting)
  Large overhead (for each packet)
  Unpredictable: no quality of service guarantee (throughput, end-to-end delay)
  Unfair (starvation)
  Unstable (unbounded queues)
11

## Slide 12: Research goals
Full system solution for specific video streaming problem:
Inputs gathering
Scheduling & Routing computation
Flow control
Simulation
Results analysis
12

## Slide 13: Solution sketch – Time division
Divide time unit into slots and in each time slot schedule a non-interfering set of links
Example:
  Slot 1: Node 1 send to node 22 in channel 2, rate 48Mbps in stream 3
  Slot 1: Node 10 send to node 2 in channel 2, rate 6Mbps in stream 5
  Slot 2: ….
Compute schedule table from node locations in a central node and broadcast to all nodes
Nodes follow schedule periodically
13

## Slide 14: Wireless interference model
Signal-to-Interference-and-Noise (SINR) Ratio model
u transmits to v while group S also transmits:
Message succeeds if SINR(u,v,S) > βm
P - transmission power
d(u,v) – distance between node u and v
N – thermal noise
- signal decay exponent (usually 2-6)
βm – minimum SNR for modulation scheme
14
Difficult for computation

## Slide 15: Wireless interference model
Protocol (Graph) model
Reception radius – upper bound on distance of transmitter
Interference radius – reception is successful only if no other transmitter within interference radius
Reception
radius
Interference
radius
Actual
Interference
15

## Slide 16: Graph model - problems
Optimistic
  Ignores the additive effect of multiple interferences
Pessimistic
  Excludes concurrent communication of two neighboring links
16

## Slide 17: Adjusted interference model
17
Chart: SNR [dB]
| 20 | 19 | 18 | 17 | 16 | 15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
1-PER | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.97 | 0.97 | 0.96 | 0.95 | 0.94 | 0.92 | 0.85 | 0.25 | 0.2 | 0.1 | 0 | 0 | 0 | 0 | 0
Nonlinear behavior –
“waterfall”
17
17
Interference radius
depends on
SINR
(distance)

## Slide 18: WiFi adjusted interference model
interference set Vu,v,m of the link e = (u,v,m)
Vu,v,m {x ∈ V \ {u} |SINR(u, v, {x}) < μβm or
SINR(v, u, {x}) < μβ0}
Interfering set of edge to link e :
Iu,v,m {e′ = (u′, v′,m′) |
{u′, v′} ∩ (Vu,v,m∪ Vv,u,m ) ≠∅} \ {(u, v,m)}
18

## Slide 19: Routing & Scheduling
Formalize linear program:
19
Flow along edge e, in channel f for stream i

## Slide 20: Linear Program (cont.)
20
Capacity constraint
Flow conservation

## Slide 21: Conflict constraint
flow/capacity: used time slice
Only single channel used for transmission
No transmission done on interfering edges simultaneously
21

## Slide 22: Linear Program (cont.)
Solve LP for maximum ρ
22
Demand for stream i
Supply ratio for stream i, fraction of supplied demand

## Slide 23: Routing & Scheduling algorithm
Formulate linear program (LP) for max-min throughput (graph model).
Output:
Need to compute scheduling table that supports the flow. (rounding problem)
23

## Slide 24: Greedy scheduler
Greedy coloring of paths
  Scan the links and frequency channels
  Assign slots to each link and frequency channel
Example problem: (Period time: 1 sec.)
  Slot 4: A -> B
  Slot 3: B -> C
  Slot 2: C -> D
  Slot 1: D -> E
24
A
B
C
D
E

## Slide 25: Greedy scheduler
Example problem: (Period time: 1 sec.)
  Slot 4: A -> B
  Slot 3: B -> C
  Slot 2: C -> D
  Slot 1: D -> E
25
A
B
C
D
E
0.75sec

## Slide 26: Greedy scheduler
Example problem: (Period time: 1 sec.)
  Slot 4: A -> B
  Slot 3: B -> C
  Slot 2: C -> D
  Slot 1: D -> E
26
A
B
C
D
E
1.5sec

## Slide 27: Greedy scheduler
Example problem: (Period time: 1 sec.)
  Slot 4: A -> B
  Slot 3: B -> C
  Slot 2: C -> D
  Slot 1: D -> E
27
A
B
C
D
E
2.25sec

## Slide 28: Greedy scheduler
Example problem: (Period time: 1 sec.)
  Slot 4: A -> B
  Slot 3: B -> C
  Slot 2: C -> D
  Slot 1: D -> E
28
A
B
C
D
E
3sec
Large latency

## Slide 29: Better schedule
Example test case: (Period time: 1 sec.)
  Slot 1: A -> B
  Slot 2: B -> C
  Slot 3: C -> D
  Slot 4: D -> E
29
A
B
C
D
E
0sec

## Slide 30: Better schedule
Example test case: (Period time: 1 sec.)
  Slot 1: A -> B
  Slot 2: B -> C
  Slot 3: C -> D
  Slot 4: D -> E
30
A
B
C
D
E
0.25sec

## Slide 31: Better schedule
Example test case: (Period time: 1 sec.)
  Slot 1: A -> B
  Slot 2: B -> C
  Slot 3: C -> D
  Slot 4: D -> E
31
A
B
C
D
E
0.5sec

## Slide 32: Better schedule
Example test case: (Period time: 1 sec.)
  Slot 1: A -> B
  Slot 2: B -> C
  Slot 3: C -> D
  Slot 4: D -> E
32
A
B
C
D
E
0.75sec

## Slide 33: Path-peeling scheduler
Decomposes each flow into flow paths such that the flow along each path equals the bottleneck, i.e., the minimum packets-per-slot(e) along the path. denote the decomposition.
While not all the flow is scheduled:
  For i = 1 to k do:
  If P(i) ≠ then schedule a path p P(i) and remove p from P(i).
33

## Slide 34: Routing & Scheduling
Approximately computed in graph model.
Does the result work in the physical (SINR) model ?
34

## Slide 35: Simulator
OMNET++/MiXiM – event driven network simulator
Extensible (C++)
Built-In wireless protocols (802.11b-Mac / Phy )
Wireless signal model (noise , interference , fading)
Mobility
Fast - Models packets (not symbols)
35

## Slide 36: System stability
Successful delivery is a random variable.
white noise in channel
802.11 random quiet periods
Fluctuations in number of packets sent in each slot incur instable queue lengths
Flow control algorithm
Goal: stabilize queue size.
36

## Slide 37: Flow Control algorithm
At the end of each schedule period each node locally performs (per stream):
  Counts #packets transmitted along outgoing & incoming edges.
  Sends updated requests for incoming link rates.
  Drops the oldest packets from queue so that all pending packets are delivered within the next period.
37

## Slide 38: Flow Control algorithm example
End of schedule period
Values indicate data transmitted across edges during last period (per stream)
38
0.3Mb
0.7Mb
1Mb
0.5Mb
0.4Mb
1Mb
0.8Mb

## Slide 39: Flow Control algorithm example
End of schedule period
Values indicate data transmitted across edges during last period (per stream)
Update step #1:
39
0.3Mb
0.7Mb
1Mb
0.5Mb
0.4Mb
1Mb
0.8Mb
0.9Mb min(0.5+0.4,1)

## Slide 40: Flow Control algorithm example
End of schedule period
Values indicate data transmitted across edges during last period (per stream)
Update step #2:
40
0.3Mb
0.7Mb
1Mb
0.5Mb
0.4Mb
0.9Mb
0.8Mb
0.9Mb
1Mb

## Slide 41: Flow Control algorithm example
End of schedule period
Values indicate data transmitted across edges during last period (per stream)
Update step #3:
41
0.3Mb
1Mb
0.5Mb
0.4Mb
0.9Mb
0.8Mb
0.9Mb
1Mb
0.7Mb
3/10*0.9Mb
7/10*0.9Mb

## Slide 42
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
32
33
34
35
36
37
38
39
40
41
42
43
44
45
46
47
48
49
Example Input scenario –
Nodes spaced equally on grid with random requests
0
1Km
1Km
Example
Transmission
Range

## Slide 43: Queue size (one stream/different nodes)
With
flow control
Without
flow control
43

## Slide 44: End-to-end delay (one stream)
With
flow
control
Without
flow
control
44

## Slide 45: Flow-control rate changes over time
45

## Slide 46: Drop rate (worst stream)

## Slide 47: End-to-End delay (per scheduler)
47

## Slide 48: Summary
Routing & scheduling approximation algorithm
Feasible in physical model (by simulation)
Local flow control algorithm
Support real-time video streaming requirements
48

## Slide 49: Questions ?
49

## Slide 50: Backup slides
50

## Slide 51: Video playback example
51

## Slide 52: WiFi adjusted interference model
interference set Vu,v,m of the link e = (u,v,m)
Vu,v,m {x ∈ V \ {u} |SINR(u, v, {x}) < μβm or
SINR(v, u, {x}) < μβ0}
Interfering set of edge to link e :
Iu,v,m {e′ = (u′, v′,m′) |
{u′, v′} ∩ (Vu,v,m∪ Vu,v,m ) ≠∅} \ {(u, v,m)}
52

## Slide 53: Hidden node problem
A and B can communicate with N
A can’t “hear” B
B can’t hear A
A and B May
attempt to
transmit un the
same time and interfere
with each other!
53
A
B
N

## Slide 54: Routing
NP Hard problem in general
Formalize constraints:
  Flow in equals flow out
  Radio is not used simultaneously for transmit and receive and not used in more than one channel
  Flow is smaller or equal edge capacity
  No conflict between transmitting nodes - by interfering edges induces by graph interference model (adjusted for WiFi- both ends transmit and multiple MCS)
54

## Slide 55
Routing result

## Slide 56: Throughput per stream
56
Without flow control
With flow control
May even increase ratio

## Slide 57: End-to-end delay histogram (one stream)
With flow control
Without flow control

## Slide 58: Routing & Scheduling
Formalize linear program:
58
Flow along edge e, in channel f for stream i
min i Ρi
2’nd target constant
Demand for stream i
Supply ratio for stream i, fraction of supplied demand

## Slide 59: Linear Program (cont.)
59
Capacity constraint
Flow conservation
Conflict constraint

## Slide 60: Flow Control algorithm - definitions
P(e,s,t) the number of packets belonging to stream s sent along the link e during the period t
P+(e,s,t) the maximum number of packets belonging to stream s that can be sent along the link e during the period t
P+(e, s, t) > P(e, s, t) iff the relevant queue is empty when a packet is scheduled, if no schedule for s on e then P+(e, s, t)=0
60

## Slide 61: Flow Control algorithm prelim.
Algorithm is executed locally for all nodes
Each node has a queue per stream
R(e, s) specifies the number of packets from stream s that the node is willing to receive along the link e in the next period t + 1
Initialize: for all e ∈ Ein(v)
R(e, s) ← [scheduler computed rate]
61

## Slide 62: Flow Control algorithm
For t = 1 to ∞ do
Measure P(e, s, t) for every e ∈ E(v), and P+(e, s, t) for every e ∈ Eout(v).
Receive P+(e, s, t) for every e ∈ Ein(v), and R(e, s) for every e ∈ Eout(v).
Rin ← min{∑e∈Eout(v) R(e, s),∑e∈Eout(v) P+(e, s, t), ∑e∈Ein (v) P+(e, s, t) }.
62

## Slide 63: Flow Control algorithm
In addition at the end of each such round we drop the oldest packets from Q(v, s), if needed, so that |Q(v, s)| ≤ Rin
Intuitively the algorithms controls the rates and queues using minor changes according to what the wireless channels and queues can sustain.
63

## Slide 64: Packet-Error-Rate / Signal-to-Noise Ratio
.
Chart: SNR [dB]
| 19.651920000000008 | 18.651920000000008 | 17.155950000000008 | 15.996530000000003 | 14.906370000000001 | 13.877690000000005 | 12.903970000000001 | 11.979640000000003 | 11.09 | 10.26 | 9.690100000000001 | 9.4586000000000006 | 7.9531999999999998 | 7.2448399999999982 | 6.5629799999999978 | 5.9067500000000015 | 5.2714800000000004 | 4.6585899999999976 | 3.4909999999999997 | 2.9349499999999993 | 2.3948999999999989 | 1.9800000000000002 | 1.36 | 0.86000000000000021
54Mbps | 0.0001 | 0.038 | 0.98 | 0.98 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
48Mbps | 0.0001 | 0.0001 | 0.0001 | 0.38 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
36Mbps | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.095 | 0.97 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
24Mbps | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.026 | 0.56 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
18Mbps | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.14 | 0.31 | 0.74 | 1 | 1 | 1 | 1 | 1 | 1 | 1
12Mbps | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.96 | 1 | 1 | 1 | 1 | 1
9Mbps | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.04 | 0.145 | 0.98 | 1 | 1
6Mbps | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 1

## Slide 65
Chart: Raw Rate (Mbps)
| 6 | 9 | 12 | 18 | 24 | 36 | 48 | 54
Simulator | 4.0628 | 5.3863 | 7.1164 | 9.3073 | 11.4279 | 14.2289 | 15.462 | 16.5702
Calculation | 4.1198 | 5.6837 | 7.0153 | 9.1616 | 10.8162 | 13.2002 | 14.8352 | 15.474
Raw Rate vs. Actual Rate
Payload size 1KB *

## Slide 66
Previous work
LP(graph) + greedy coloring – constant approximation
PTAS – impractical due to rounding problem
Routing in SINR – logarithmic approximation with uniform power
simulations in graph model

## Slide 67
Key Contributions
Adjusted graph model
SINR simulations
Path peeling scheduler
Flow control
Analysis for Video