## Slide 1: Real Time Video Streaming in Multi hop Ad-Hoc Wireless networks
Yaniv Fais
Under supervision of Prof. Guy Even
Joint work with Prof. Guy Even, Moti Medina,
Moni Shachar and Alexander Zadorojniy

## Slide 2: Agenda
Problem Definition
  Real-Time Video
  WiFi introduction
Routing & Scheduling
  Interference models
Simulator
  Flow Control
Experimental results
  Video transmission
2

## Slide 3: Problem Definition
Ad-Hoc Wireless Network model
  Nodes in the plane with single radio
  Multiple radio channels
  Interference is an important issue
  Nodes know location and time (using GPS)
3

## Slide 4: Problem Definition II
Input: Nodes + real-time video transmission requests:
  Source , Destination , Bandwidth
  (Source and destinations are not neighbors)
Goal: serve requests (max-min throughput)
4

## Slide 5: Real-Time Video characteristics
High-bandwidth
  ~1Mbps after encoding
Require: low end-to-end delay
  Few seconds at most
Require: small packet-loss
  < 5%
Adjustable bit rate because encoder can be controlled (variable quality and compression ratio)
5

## Slide 6: IEEE 802.11g (WiFi)
Carrier sense multiple access with collision detection (CSMA/CD)
Transmitter sends Request To Send (RTS)
6

## Slide 7: IEEE 802.11g (WiFi)
Receiver sends “Clear To Send” (CTS)
All other nodes remain “quiet” throughout packet transmission
7

## Slide 8: IEEE 802.11g (WiFi)
Transmitter sends frame with payload data (large frame – several KB)
8

## Slide 9: IEEE 802.11g (WiFi)
Receiver sends “Acknowledge” (ACK) packet once complete
9

## Slide 10: IEEE 802.11g (WiFi)
Distributed protocol that avoids collisions
But: (In multi-hop setting)
  Large overhead (for each packet)
  Unpredictable: no quality of service guarantee (throughput, end-to-end delay)
  Unfair (starvation)
  Unstable (unbounded queues)
10

## Slide 11: Solution sketch – Time division
Divide time unit into slots and in each time slot schedule a non-interfering set of links
Example:
  Slot 1: Node 1 send to node 22 in channel 2, rate 48Mbps in stream 3
  Slot 1: Node 10 send to node 2 in channel 2, rate 6Mbps in stream 5
  Slot 2: ….
Compute schedule table from node locations in a central node and broadcast to all nodes
Nodes follow schedule periodically
11

## Slide 12: Wireless interference model
Protocol (Graph) model
* Reception radius – upper bound on distance of transmitter
Interference radius – reception is successful only if no other transmitter within interference radius
But in reality signal goes beyond this range!
Reception
radius
Interference
radius
Actual
Interference
12

## Slide 13: Graph model - problems
Optimistic
  Ignores the additive effect of multiple interferences
Pessimistic
  Excludes concurrent communication of two neighboring links
13

## Slide 14: Wireless interference model
Signal-to-Interference-and-Noise (SINR) Ratio model
u transmits to v while group S also transmits:
Message succeeds if SINR(u,v,S) > βm
P - transmission power
d(u,v) – distance between node u and v
N – thermal noise
- signal decay exponent (usually 2-6)
βm – minimum SNR for modulation scheme
14

## Slide 15: Routing & Scheduling
Formalize linear program:
15
Flow along edge e, in channel f for stream i
min i Ρi
2’nd target constant
Demand for stream i
Supply ratio for stream i, fraction of supplied demand

## Slide 16: Linear Program (cont.)
16
Capacity constraint
Flow conservation
Conflict constraint

## Slide 17: Routing & Scheduling algorithm
Formulate linear program (LP) for max-min throughput (graph model).
Output:
Need to compute scheduling table that supports the flow.
17

## Slide 18: Path-peeling scheduler
Decomposes each flow into flow paths such that the flow along each path equals the bottleneck, i.e., the minimum packets-per-slot(e) along the path. denote the decomposition.
While not all the flow is scheduled:
  For i = 1 to k do:
  If P(i) ≠ then schedule a path p P(i) and remove p from P(i).
Minimizes end-to-end
18

## Slide 19: Routing & Scheduling
Computed in graph model and achieves a constant approximation ratio.
Does the result work in the physical (SINR) model ?
19

## Slide 20: Simulator
OMNET++/MiXiM – event driven network simulator
Extensible (C++)
Built-In wireless protocols (802.11b-Mac / Phy )
Wireless signal model (noise , interference , fading)
Mobility
Fast - Models packets (not symbols)
20

## Slide 21: Flow Control
Successful delivery is a random variable.
Real channel suffers from white noise - different than channel with fixed flow-capacity
802.11 random quiet periods
Fluctuations in number of packets sent in each slot incur instable queue lengths
Goal: stabilize queue size.
21

## Slide 22: Flow Control algorithm
At the end of each schedule period each node (per stream):
  Counts #packets transmitted along outgoing & incoming edges.
  Sends updated requests for incoming link rates.
  Drops the oldest packets from queue so that all pending packets are delivered within the next period.
22

## Slide 23
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
32
33
34
35
36
37
38
39
40
41
42
43
44
45
46
47
48
49
Example Input scenario –
Nodes spaced equally on grid with random requests
0
500m
1Km
500m
1Km
Example
Transmission
Range

## Slide 24: End-to-End delay (per scheduler)
24

## Slide 25: Queue size (one stream/different nodes)
With
flow control
Without
flow control
25

## Slide 26: End-to-end delay (one stream)
With
flow
control
Without
flow
control
26

## Slide 27: Flow-control rate changes over time
27

## Slide 28: Drop rate (worse stream)

## Slide 29: Summary
Routing & scheduling approximation algorithm
Feasible in physical model (by simulation)
Local flow control algorithm
Support real-time video streaming requirements
29

## Slide 30: Questions ?
30

## Slide 31: Backup slides
31

## Slide 32: Video playback example
32

## Slide 33: WiFi adjusted interference model
interference set Vu,v,m of the link e = (u,v,m)
Vu,v,m {x ∈ V \ {u} |SINR(u, v, {x}) < μβm or
SINR(v, u, {x}) < μβ0}
Interfering set of edge to link e :
Iu,v,m {e′ = (u′, v′,m′) |
{u′, v′} ∩ (Vu,v,m∪ Vu,v,m ) ≠∅} \ {(u, v,m)}
33

## Slide 34: Hidden node problem
A and B can communicate with N
A can’t “hear” B
B can’t hear A
A and B May
attempt to
transmit un the
same time and interfere
with each other!
34
A
B
N

## Slide 35: Routing
NP Hard problem in general
Formalize constraints:
  Flow in equals flow out
  Radio is not used simultaneously for transmit and receive and not used in more than one channel
  Flow is smaller or equal edge capacity
  No conflict between transmitting nodes - by interfering edges induces by graph interference model (adjusted for WiFi- both ends transmit and multiple MCS)
35

## Slide 36
Routing result

## Slide 37: Throughput per stream
37
Without flow control
With flow control
May even increase ratio

## Slide 38: Flow Control algorithm - definitions
P(e,s,t) the number of packets belonging to stream s sent along the link e during the period t
P+(e,s,t) the maximum number of packets belonging to stream s that can be sent along the link e during the period t
P+(e, s, t) > P(e, s, t) iff the relevant queue is empty when a packet is scheduled, if no schedule for s on e then P+(e, s, t)=0
38

## Slide 39: Flow Control algorithm prelim.
Algorithm is executed locally for all nodes
Each node has a queue per stream
R(e, s) specifies the number of packets from stream s that the node is willing to receive along the link e in the next period t + 1
Initialize: for all e ∈ Ein(v)
R(e, s) ← [scheduler computed rate]
39

## Slide 40: Flow Control algorithm
For t = 1 to ∞ do
Measure P(e, s, t) for every e ∈ E(v), and P+(e, s, t) for every e ∈ Eout(v).
Receive P+(e, s, t) for every e ∈ Ein(v), and R(e, s) for every e ∈ Eout(v).
Rin ← min{∑e∈Eout(v) R(e, s),∑e∈Eout(v) P+(e, s, t), ∑e∈Ein (v) P+(e, s, t) }.
40

## Slide 41: Flow Control algorithm
In addition at the end of each such round we drop the oldest packets from Q(v, s), if needed, so that |Q(v, s)| ≤ Rin
Intuitively the algorithms controls the rates and queues using minor changes according to what the wireless channels and queues can sustain.
41

## Slide 42: End-to-end delay histogram (one stream)
With flow control
Without flow control

## Slide 43: Packet-Error-Rate / Signal-to-Noise Ratio
.
Chart: SNR [dB]
| 19.651920000000008 | 18.651920000000008 | 17.155950000000008 | 15.996530000000003 | 14.906370000000001 | 13.877690000000005 | 12.903970000000001 | 11.979640000000003 | 11.09 | 10.26 | 9.690100000000001 | 9.4586000000000006 | 7.9531999999999998 | 7.2448399999999982 | 6.5629799999999978 | 5.9067500000000015 | 5.2714800000000004 | 4.6585899999999976 | 3.4909999999999997 | 2.9349499999999993 | 2.3948999999999989 | 1.9800000000000002 | 1.36 | 0.86000000000000021
54Mbps | 0.0001 | 0.038 | 0.98 | 0.98 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
48Mbps | 0.0001 | 0.0001 | 0.0001 | 0.38 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
36Mbps | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.095 | 0.97 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
24Mbps | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.026 | 0.56 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
18Mbps | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.14 | 0.31 | 0.74 | 1 | 1 | 1 | 1 | 1 | 1 | 1
12Mbps | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.96 | 1 | 1 | 1 | 1 | 1
9Mbps | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.0001 | 0.04 | 0.145 | 0.98 | 1 | 1
6Mbps | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 0.017 | 1

## Slide 44
Chart: Raw Rate (Mbps)
| 6 | 9 | 12 | 18 | 24 | 36 | 48 | 54
Simulator | 4.0628 | 5.3863 | 7.1164 | 9.3073 | 11.4279 | 14.2289 | 15.462 | 16.5702
Calculation | 4.1198 | 5.6837 | 7.0153 | 9.1616 | 10.8162 | 13.2002 | 14.8352 | 15.474
Raw Rate vs. Actual Rate
Payload size 1KB *